DS-K1100 Series Card Reader

Installation Guide

UD.6L0206D1147A02

User Manual

About this Manual

This Manual is applicable to Card Reader.

The Manual includes instructions for using and managing the product. Pictures, charts, images and all other information hereinafter are for description and explanation only. The information contained in the Manual is subject to change, without notice, due to firmware updates or other reasons. Please find the latest version in the company website.

Please use this user manual under the guidance of professionals.

Legal Disclaimer

REGARDING TO THE PRODUCT WITH INTERNET ACCESS, THE USE OF PRODUCT SHALL BE WHOLLY AT YOUR OWN RISKS. OUR COMPANY SHALL NOT TAKE ANY RESPONSIBILITES FOR ABNORMAL OPERATION, PRIVACY LEAKAGE OR OTHER DAMAGES RESULTING FROM CYBER ATTACK, HACKER ATTACK, VIRUS INSPECTION, OR OTHER INTERNET SECURITY RISKS; HOWEVER, OUR COMPANY WILL PROVIDE TIMELY TECHNICAL SUPPORT IF REQUIRED.

SURVEILLANCE LAWS VARY BY JURISDICTION. PLEASE CHECK ALL RELEVANT LAWS IN YOUR JURISDICTION BEFORE USING THIS PRODUCT IN ORDER TO ENSURE THAT YOUR USE CONFORMS THE APPLICABLE LAW. OUR COMPANY SHALL NOT BE LIABLE IN THE EVENT THAT THIS PRODUCT IS USED WITH ILLEGITIMATE PURPOSES.

IN THE EVENT OF ANY CONFLICTS BETWEEN THIS MANUAL AND THE APPLICABLE LAW, THE LATER PREVAILS.

0101011050112

Regulatory Information

FCC Information

FCC compliance: This equipment has been tested and found to comply with the limits for a digital device, pursuant to part 15 of the FCC Rules. These limits are designed to provide reasonable protection against harmful interference when the equipment is operated in a commercial environment. This equipment generates, uses, and can radiate radio frequency energy and, if not installed and used in accordance with the instruction manual, may cause harmful interference to radio communications. Operation of this equipment in a residential area is likely to cause harmful interference in which case the user will be required to correct the interference at his own expense.

FCC Conditions

This device complies with part 15 of the FCC Rules. Operation is subject to the following two conditions:

1. This device may not cause harmful interference.

2. This device must accept any interference received, including interference that may cause undesired operation.

EU Conformity Statement

This product and - if applicable - the supplied accessories too are marked with "CE" and comply therefore with the applicable   harmonized European standards listed under the EMC Directive 2004/108/EC, the RoHS Directive 2011/65/EU.

2012/19/EU (WEEE directive): Products marked with this symbol cannot be disposed of as unsorted municipal waste in the European Union. For proper recycling, return this product to your local supplier upon the purchase of equivalent new equipment, or dispose of it at designated collection points. For more information see: www.recyclethis.info.

2006/66/EC (battery directive): This product contains a battery that cannot be disposed of as unsorted municipal waste in the European Union. See the product documentation for specific battery information. The battery is marked with this symbol, which may include lettering to indicate cadmium (Cd), lead (Pb), or mercury (Hg). For proper recycling, return the battery to your supplier or to a designated collection point. For more information see: www.recyclethis.info.

Industry Canada ICES-003 Compliance

This device meets the CAN ICES-3 (A)/NMB-3(A) standards requirements.

# Preventive and Cautionary Tips

To guarantee the card reader works properly, please read and obey the notes below.

- If the card reader is powered by the controller, the power supply distance is recommended to be no longer than 100m. If the distance is longer than 100m, you are advised to power the card reader by external 12V (range: -%10 ~ +%10) DC power supply, which is nonswitched and linear.

- To guarantee the communication between the controller and the card reader, you must use RVVP cable above 0.5 to connect them.

- If the card reader is installed outside or in environment easy to permeable, it is advisable to install a waterproof shield.

- If you need to install several card readers, the distance among them must over 30cm.

- To reduce the noise in long distance transmission, the shield of cable should connect to the GND of both controller and card reader terminal.

01010110600112

Content

Preventive and Cautionary Tips	iv

Chapter 1	Introduction	2

1.1	Front View	2

1.2	Rear View	4

1.3	Side View	8

Chapter 2	Installation	9

2.1	Installing PSAM Card	9

2.2	Introduction for DIP Switch	10

2.3	Definition of Cable	11

2.4	Wiring Cables	11

2.5	Installing Card Reader	13

Chapter 3	Sound Prompt and Indicator	15

# Introduction

DS-K1100 series card reader is a kind of high-performance product, with a 32 bit high-speed processor. It communicates with access controller via either RS-485 protocol or Wiegand protocol. And a build-in tamper-proof module helps to protect card reader from malicious damage. As to the physical appearance, the PC+ABS material makes water proof and dust proof possible in poor environment.

## Front View

The front view of DS-K1101 series card reader is shown below:

| DS-K1101MK/DS-K1101CK | DS-K1101M/DS-K1101C |
| --- | --- |

The front view of DS-K1102 series card reader is shown below:

| DS-K1102MK/DS-K1102CK | DS-K1102M/DS-K1102C |
| --- | --- |

The front view of DS-K1103 series card reader is shown below:

| DS-K1103MK/DS-K1103CK | DS-K1103M/DS-K1103C |
| --- | --- |

The front view of DS-K1104 series card reader is shown below:

| DS-K1104MK/DS-K1104CK | DS-K1104M/DS-K1104C |
| --- | --- |
| The front view of DS-K1104 series card reader is shown below: |
| DS-K1106M/DS-K1106C/ DS-K1106S |  |

## Rear View

The rear view of card reader is shown below:

Rear View of DS-K1101 Series

Rear View of DS-K1102 Series

Rear View of DS-K1103 Series

Rear View of DS-K1104 Series

Description of Rear View

| No. | Name |
| --- | --- |
| 1 | Cable Interface of RS-485, Power, LED Control, etc. |
| 2 | Buzzer |
| 3 | Tamper-proof Module |
| 4 | DIP Switch |
| 5 | PSAM Card Slot (available for CPU card reader) |

The rear view of DS-K1106 series card reader is shown below:

              - Rear View of DS-K1106 Series

| No. | Name |
| --- | --- |
| 1 | PSAM Card Slot (available for CPU card reader) |
| 2 | DIP Switch |
| 3 | Cable Interface of RS-485, Power, LED Control, etc. |
| 4 | Serial Port |

## Side View

The side view of card reader is shown below:

| DS-K1101 Series | DS-K1102 Series |
| --- | --- |
| DS-K1103 Series | DS-K1104 Series |

# Installation

## Installing PSAM Card

PSAM card slot is only available for CPU card reader.

Insert the PSAM card into the slot according to the direction shown below.

PSAM Card Slot

## Introduction for DIP Switch

The DIP switch module is shown below. The No. of DIP switch from left to right is 1 ~ 8.

DIP Switch Module

Description of DIP Switch

| Icon | Description |
| --- | --- |
|  | Represent 1 in binary mode |
|  | Represent 0 in binary mode |

For example, binary value of the following status is: 0000 1100.

DIP Switch Module

Description of DIP Switch

| No. | Description | DIP Switch Status |
| --- | --- | --- |
| 1 ~ 4 | Address of RS-485 | 1: 1 0: 0 |
| 5 | Read card No. or file in card. (Only available for CPU card reader.) | 1: read card No; 0: read file in card. |
| 6 | Wiegand protocol or RS-485 protocol. | 1: Wiegand protocol; 0: RS-485 protocol. |
| 7 | Wiegand Protocol (available when No. 6 is 1) | 1: Wiegand protocol of 26-bit; 0: Wiegand protocol of 34-bit. |
| 8 | Matched Resistance (available for RS-485 protocol) | 1: Enable; 0: Disable. |

## Definition of Cable

The description of 10 cables is shown below.

Description of Cable

| Color | Description |
| --- | --- |
| Yellow | RS-485+ |
| Brown | Blue LED Control (available for Wiegand Protocol) |
| Blue | RS-485- |
| Purple | Beep Control (available for Wiegand Protocol) |
| Gray | Case Sensor (available for Wiegand Protocol) |
| Green | Wiegand W0 (available for Wiegand Protocol) |
| White | Wiegand W1 (available for Wiegand Protocol) |
| Black | GND |
| Orange | Red LED Control (available for Wiegand Protocol) |
| Red | PWR (DC +12V) |

## Wiring Cables

Purpose:

Wire the cables between controller and card reader, thus to establish the communication between them.

Steps for RS-485 communication mode:

- Set the DIP switch of No. 6 as 0.

- Set the DIP switch of No. 1 ~ 5 for RS-485 address and reading card mode. For details, please refer to 2.2 Introduction for DIP Switch.

- Wire the cable between controller and card reader as shown below.

Wiring for RS-485 Communication Mode

Steps for Wiegand communication mode:

- Set the DIP switch of No. 6 as 1.

- Set the DIP switch of No. 5 and 7 for reading card mode and Wiegand protocol. For details, please refer to 2.2 Introduction for DIP Switch.

- Wiring the cable between controller and card reader as shown below.

Wiring for Wiegand Communication Mode

## Installing Card Reader

Before you start:

Set the DIP switch. For details, refer to 2.2 Introduction for DIP Switch.

Installation for DS-K1101/ 02/ 03/ 04 series card reader

Steps:

| Fix the plate on the wall or other place. |  |
| --- | --- |
| Connect the cables between controller and card reader. For details, refer to 2.4 Wiring Cables. |  |
| Push the card reader to match the fixed plate. |  |
| Fasten the screw to keep the components together. |  |

Installation for DS-K1106 series card reader

Steps:

| Fix the gang box on the wall or other place. |  |
| --- | --- |
| Connect the cables between controller and card reader. For details, refer to 2.4 Wiring Cables. Push the card reader to match the fixed gang box. Fasten the screw to keep the components together. |  |
| Fix the side cover onto the card reader, press the cover to make it tightly fit the reader. |  |

# Sound Prompt and Indicator

After the card reader is powered on, LED status indicator will turn blue and blink for 1 time. Then it will turn red and blink for 3 times. At last the buzzer will send out a beep sound indicating the starting up process is completed.

During using the card reader, it will send out different sounds prompt and the LED indicator on it have different statuses. You can refer to tables below for detailed information.

Description of Prompt Sound

| Sound Prompt | Description |
| --- | --- |
| One beep | RS-485 protocol: Pressing keys prompt; Swiping card prompt; Time out prompt for pressing keys or swiping card. Wiegand protocol: Pressing keys prompt; Swiping card prompt. |
| Two rapid beeps | The operation of pressing keys or swiping card is valid. |
| Three slow beeps | The operation of pressing keys or swiping card is invalid. |
| Rapidly continuous beeps | Alarm of tamper-proof. |
| Slowly continuous beeps | The card reader is unencrypted. |

Description of LED Indicator

| LED Indicator Status | Description |
| --- | --- |
| Blue and blinking | Card reader is working normally. |
| Solid blue | The operation of pressing keys or swiping card is valid. |
| Solid red | The operation of pressing keys or swiping card is invalid. |
| Red and blinking | For RS-485 protocol: Registering failed or card reader is offline. |
| Red and Keeping rapidly blinking | Available for reading file mode of CPU card: PSAM is not inserted or undetected. |
| Red and keeping rapidly blinking and slowly beeps | Failed to get key files of PSAM card; Failed to detect the PSAM card. |